## Slide 1: Section 4: Models for Recovery and Repair
Recall from P-102 that simplest aleatory model for time as a random variable is the exponential distribution
T ~ exp()
Unknown parameter is , which is recovery rate in present context
  MTTR = 1/
Data is series of times for recovery or repair, assumed to be random sample from exp() distribution
For Bayesian inference, need prior distribution for 
  Conjugate prior is gamma distribution
  Jeffreys prior is (improper) gamma(0, 0)
  CNI prior doesn’t exist
    Maximum entropy prior is exp() where  is specified mean constraint
  Nonconjugate prior
Notes: Use Shannon entropy, whereas CNI uses Jaynes entropy, with Jeffreys as reference prior.
Note that  is commonly used for repair rate and  is used for failure rate.

## Slide 2: DAG Representation
λ
Vector of times

## Slide 3: OpenBUGS Script
Exponential model.odc
model {
for(i in 1:N) {
time[i] ~ dexp(lambda) #Exponential distribution for each time 1 to N
}
lambda ~ dgamma(0.0001, 0.0001) #Jeffrey’s prior
MTTR <- 1/lambda
}
data
list(time=c(105, 1, 1263, 72, 37, 814, 1.5, 211, 330, 7929, 296, 1, 120, 1), N = 14)
inits
list(lambda=1.E-3)
list(lambda=5.E-3)
Notes: Point out initial values are needed for Jeffreys prior in this case. Two chains used simply for illustration.

## Slide 4: Results

## Slide 5: What is Distribution of New (i.e., Predicted) Time, Given Observed Times?
The distribution for MTTR found previously describes the uncertainty in the mean time to recovery/repair
Distribution of new time is obtained by averaging over the posterior distribution for :
Called posterior predictive distribution
  Will use this extensively for model-checking
Notes: This is the second time the idea of the posterior predictive distribution has been slipped in.

## Slide 6: DAG Model for Predicted Time

## Slide 7: Results for Predicted Time
Add the line
# Predicted failure time from posterior predictive distribution
t.pred ~ dexp(lambda)
Note wider uncertainty interval for t.pred

## Slide 8: Specifying a Model
From experience, recovery time does not tend to be exponential
  Recovery rate [h(t)] often decreases with time after the initiator
    h(t) = f(t)/[1 – F(t)]
  Common models for non-constant recovery rate
    Weibull
    Gamma
    Lognormal

## Slide 9: Alternatives to Exponential Model - Weibull
T ~ Weibull(, )
  f(t) =   t-1 exp(- t)
  F(t) = 1 – exp (- t)
  E(T) = -1/(1 + 1/)
  For  =1, reduces to exponential()
  Recovery rate is function of time
    h(t) =   t-1
     < 1  h(t) decreasing with time
     > 1  h(t) increasing with time
Notes: Using Weibull parameterization needed by OpenBUGS.

## Slide 10: Further Weibull Parameters
Previous slide uses parameters defined for OpenBUGS, which were convenient for Bayesian analysis in the days before MCMC and for some reason the developers used
Alternative parameterization uses  = λ-1/ , λ =- , giving
  f(t) = (/)(t/)-1exp[-(t/)]
  F(t) = 1 - exp [-(t/)]
  E(T) = (1 + 1/)
  h(t) = (/)(t/)-1
 > 0
λ > 0

## Slide 11: Alternatives to Exponential Model - Gamma
T ~ gamma(, )
E(T) = /
For  =1, reduces to exponential()
Recovery rate is function of time
  Cannot be written in closed form
   < 1  h(t) decreasing with time
   > 1  h(t) increasing with time
 > 0
 > 0

## Slide 12: Alternatives to Exponential Model - Lognormal
T ~ lognormal(, )
  OpenBUGS uses  =  -2
F(t) = [(lnt - )]
E(T) = exp( + 1/(2))
Recovery rate is function of time
  Increases from 0 initially (often very fast), then decreases, approaching 0 asymptotically
    Approach to 0 can be very slow
  Useful when early recoveries dominate

## Slide 13: Alternatives to Exponential Model
Note that all alternatives considered have two unknown parameters
  Weibull(α, )
  Gamma(α, )
  Lognormal(, ) or Lognormal(, )
Need to specify joint prior distribution, e.g., π(, )

## Slide 14: Specifying Joint Prior via Bayesian Network
Much effort was spent in the past developing complicated joint prior distributions that reflected correlation between two parameters
With Bayesian network, we can specify independent priors and not worry about this
  In Bayesian network, parameters are independent until data is observed
  Posterior distribution will reflect proper dependence between parameters

## Slide 15: Example DAG for Lognormal Model
Notes: In terms of the Bayesian network,  and  are d-separated until the times are observed.

## Slide 16: Choosing Priors for  and 
Will use independent priors
Range of  is - to 
Range of  is 0 to 
If prior information is available, can use this
Noninformative priors are often used
  Do not use Jeffreys prior in this case
  Use Laplace (infinite uniform) prior or very diffuse normal prior for 
  Use diffuse gamma or finite uniform prior for 

## Slide 17: Choosing Priors for  and 
Easier to think in terms of  =  -0.5
  Recall that EF = e1.645 for the lognormal distribution
     = 10 corresponds to EF > 13,936,195 (wow!)
LogNorm and Weibull LOSP durations.odc
model {
for (i in 1 : N) {
time.rec[i] ~ dlnorm(mu, tau) #Lognormal model for recovery time
}
mu ~ dflat() #Diffuse prior for mu
sigma ~ dunif(0, 10)
tau <- pow(sigma, -2)
}
Notes: Point out need to check marginal posterior for  to ensure range of prior was wide enough to avoid truncation.

## Slide 18: Running the Script
We are interested in inference for two parameters, so convergence is a concern
  Will run two chains starting at different points
Check history plots for mu and sigma
Check BGR statistic
Notes: Discuss choosing initial values a bit. Mention that MLEs can be used, and these are easy to obtain for the lognormal distribution.

## Slide 19: Results
History plots after 1,000 samples
Notes: History plots don’t suggest a convergence problem.

## Slide 20: Results
BGR plots after 1,000 samples
Notes: BGR converges to approximately 1.0 and is stable.

## Slide 21: Results
Discard first 1,000 samples for burn-in, run additional 100,000 samples to estimate  and :

## Slide 22: Exercises
Use the data in “times-1.txt” in the BUGS folder for the following questions.
Assuming an exponential aleatory model, and a lognormal prior for  with a mean of 1 and error factor of 3, find the posterior mean and 90% interval for .
Assume a lognormal aleatory model with independent, diffuse priors on the lognormal parameters. Find the posterior mean and 90% interval for .

## Slide 23: Exercises
In NUREG/CR-6890, a distribution for the repair of an EDG when 2 or more EDGs are failed was simulated by sampling from two repair distributions and finding the smallest time. These smallest times were used to describe the EDG repair rate.
Let us perform a Bayesian version of this calculation. The file “EDG repair times.txt” in the BUGS folder contains 18 repair times recorded when a single EDG failed.
  Find the posterior means of the parameters of a Weibull aleatory model for these repair times. Use independent, diffuse priors for the Weibull parameters.
  Generate two, independent predicted repair times from the posterior distribution. What is the mean and 90% credible interval for each of these times?
  Define a new variable that is the minimum of each of the two times generated in part (b) by using the OpenBUGS min( ) function. What is the mean and 90% credible interval for this minimum time?
Notes: This exercise illustrates the Bayesian version of how NUREG/CR-6890 developed a Weibull distribution for the repair of an EDG when 2 or more EDGs are failed.