## Slide 1: Section 2: Introduction to Bayesian Networks and OpenBUGS
What are Bayesian networks and why are they useful?
Bayesian networks allow “math-free” analysis of complex problems
  Formulates problem as graphical model
  Lessens mathematical burden on the analyst
  Allows easier communication with non-specialists

## Slide 2: Introduction to Bayesian Networks and OpenBUGS
Networks are new way of representing old (simple) problems and allow easy analysis of new (complex) problems
Network representation of Bayes Theorem
Prior P0()

E
Observed
Value of E
L(E|)
Notes: This course does not delve into Bayesian network formalism.

## Slide 3: Why OpenBUGS?
Tool tailored for numerical analysis of Bayesian networks
OpenBUGS is a standard tool for Bayesian inference in the wider statistical community
  "OpenBUGS…has become the most popular means for numerical investigation of Bayesian inference.“ Bayesian Statistics, An Introduction, 3rd Edition, by Peter Lee
OpenBUGS is free, open-source software with a built-in interface
OpenBUGS does not require an “installation”, therefore no administrator privileges are required for the classroom environment

## Slide 4: Why OpenBUGS?
OpenBUGS is flexible, allowing new problems to be solved as they arise
  Some tension between flexibility and ease of use
  Batch mode operation possible for routine problems

## Slide 5: Prior Distributions for LOSP Example (from P-102 Course)
 LOSP ~ gamma(1.58, 43.96 reactor-critical years)
  From “Reevaluation of Station Blackout Risk at Nuclear Power Plants: NUREG/CR-6890, December 2005
  Above result is composite from several subtypes of LOSP event
pFTS ~ beta(0.957, 190)
  From S. A. Eide, “Historical Perspective On Failure Rates for US Commercial Reactor Components,” Reliability Engineering and System Safety, 80 (2003), pp. 123-132
 FTR ~ gamma(1.32,1137 hrs)
  From Eide (2003)
  Above result is composite of two rates

## Slide 6: LOSP Example Data
The observed number of LOSP events over a period of time
  1 initiating event in 9.2 operating years
The observed number of failures out of a number of demands
  1 failure to start in 75 demands
The observed number of failures in an observed total operating time
  0 failures to run in 146 running hours

## Slide 7: Summary of Bayesian Estimates for LOSP Example
Parameter | Distribution | Point Est. (Mean) | 90% Interval
LOSP | Industry Prior Posterior | 3.6E-2 yr -1 4.9E-2 yr -1 | (4.6E-3, 9.2E-2) yr -1 (1.1E-2, 1.1E-1) yr -1
pFTS | Industry Prior Posterior | 5.0E-3 7.4E-3 | (2.3E-4, 1.5E-2) (1.3E-3, 1.8E-2)
FTR | Industry Prior Posterior | 1.2E-3 hr -1 1.0E-3 hr -1 | (1.1E-4, 3.2E-3) hr -1 (9.6E-5, 2.8E-3) hr -1
        Posterior credible intervals generally shorter than those from data alone (i.e., confidence interval) or prior alone (prior credible interval)
Notes: Instructor should have students use single parameter estimation spreadsheet to rework these problems.

## Slide 8: Bayesian Network Model for LOSP Initiating Event
Also referred to as directed acyclic graph (DAG)
  Shows relationship of nodes (what influences what)
  Oval represents stochastic node
  Rectangle represents constant node
  Arrows illustrate influence (“flow of information”)
Notes: Take time to walk through this DAG slowly, pointed out what is observed (bottom node, losp) and what is inferred (lambda.losp). Discuss parent-child terminology. Note Page 13 in text.

## Slide 9: Introduction to OpenBUGS Package
BUGS = Bayesian inference Using Gibbs Sampling
Freely available software, download from
http://www.openbugs.info/w/Downloads
New developments at www.openbugs.net
  Latest version is 3.2.3
Source code available in Component Pascal
Simulates posterior distribution directly using Markov Chain Monte Carlo (MCMC) sampling (covered later)

## Slide 10: Introduction to OpenBUGS
OpenBUGS script (program) has four parts:
  Model section
  Data
  Inits (initial values for model parameters)
  Comments
    Anything preceding model section or set off with #
Script is compiled to process model and associated data

## Slide 11: Example OpenBUGS Script (LOSP-poisson update.odc in BUGS folder)
LOSP frequency from example problem
  Industry prior is gamma(1.58, 43.96 yr)
  Data: 1 event in 9.2 yr
LOSP-poisson update.odc
model {
losp ~ dpois(mu) #Poisson distribution
mu <- lambda.losp*rx.yrs #Poisson dist. parameter
lambda.losp ~ dgamma(1.58, 43.96) #Prior LOSP distribution
}
data
list(losp=1, rx.yrs=9.2)

## Slide 12: Example OpenBUGS Script (LOSP-poisson update.odc in BUGS folder)
Dissect the script
LOSP-poisson update.odc
Model defined here between { }
Note observable event and model have same name
model {
losp ~ dpois(mu) #Poisson distribution
mu <- lambda.losp*rx.yrs #Poisson dist. parameter
lambda.losp ~ dgamma(1.58, 43.96) #Prior LOSP distribution
}
data
list(losp=1, rx.yrs=9.2)

## Slide 13: Example OpenBUGS Script (LOSP-poisson update.odc in BUGS folder)
Dissect the script
LOSP-poisson update.odc
Data defined after “list” keyword
OpenBUGS “knows” that prior needs to be “updated”
model {
losp ~ dpois(mu) #Poisson distribution
mu <- lambda.losp*rx.yrs #Poisson dist. parameter
lambda.losp ~ dgamma(1.58, 43.96) #Prior LOSP distribution
}
data
list(losp=1, rx.yrs=9.2)

## Slide 14: Running the Example Script
Double-click on “model”
Select “Model – Specification” from toolbar:

## Slide 15: Running the Example Script
Specification toolbox appears on screen:
Select “Check Model”
  OpenBUGS should report “model is syntactically correct” (lower left corner of window)

## Slide 16: Running the Example Script
Double-click “list” in the data portion of the script, then select “load data”
  OpenBUGS reports “data loaded”
Select “compile”
  OpenBUGS reports “model compiled”
For such a simple model, we will let OpenBUGS generate initial values
  Select “gen inits”
    OpenBUGS reports “initial values generated, model initialized”
Leave the Specification Tool dialogue box open

## Slide 17: Running the Example Script
Select “Inference – Samples” from the toolbar
Notes: We must now tell OpenBUGS which parameters (nodes) to monitor.

## Slide 18: Running the Example Script
Type the variable name you want to monitor in the “node” box (case sensitive)
Select 1,000 burn-in samples (will discuss later)
  Type 1001 in the “beg” box

## Slide 19: Running the Example Script
Click “Set” button
Select “Model – Update” from the toolbar

## Slide 20: Running the Example Script
Update tool appears on screen
Enter number of samples
  100,000 is typical for simple problems
Increase refresh from 100 to 1000 or 10000 to speed up sampling
Select “Update”
  OpenBUGS reports “model is updating” and shows current iteration
Notes: Note that refreshing less often will sometimes decrease the analysis time drastically.

## Slide 21: Running the Example Script
Select “lambda.losp” from the list of monitored nodes on the Sample Monitor Tool
Select the desired percentiles from box on right
  Check 5th, 50th, and 95th, by holding down Ctrl key
Select “density” to get graph of posterior density

## Slide 22: Running the Example Script
Select “stats” to get posterior mean and percentiles
Compare with results from P-102
Parameter | Distribution | Mean | 90% Interval
λLOSP | Posterior | 4.9E-2 yr -1 | (1.1E-2, 1.1E-1) yr -1

## Slide 23: Bayesian Model for EDG FTS
Recall aleatory model for number of EDG failures is binomial distribution
  Unknown parameter is pFTS
  DAG model (Section 3.2.1 of Textbook)

## Slide 24: OpenBUGS Script for EDG FTS
Beta-binomial update.odc
Model {
#*****Binomial likelihood for number of failures*****
x.fts ~ dbin(p.fts, n.fts)
#*****Beta prior for p.fts*****
p.fts ~ dbeta(alpha, beta)
}
data
list(x.fts=1, n.fts=75, alpha=0.5, beta=0.5)
Notes: Have students run this model and compare with results from P-102’s Distribution Summary Worksheets

## Slide 25: Illustration of the FTS Script

## Slide 26: Conjugate Prior Exercises with BUGS
An analyst proposes a gamma(0.1, 100 Rx-yr) prior distribution for small LOCA. Using BUGS, find the posterior mean and 90% interval based on 0 small LOCAs in 2,276 Rx-yrs.
Assume that failures to start of a diesel can be described by a binomial distribution with probability of failure on demand, p.
  What is the constrained noninformative (CNI) prior if we want the mean to be 0.001?
  Using the CNI prior from part (a), and 2 failures are observed in 500 demands, use BUGS to find the posterior mean and 95% credible interval for p.
Notes: Go over documentation and help available within BUGS.
May need to remind students about the CNI prior, which is covered in P-102.

## Slide 27: Noninformative Priors with OpenBUGS
Recall Jeffreys prior distributions from P-102
  Binomial model: beta(0.5, 0.5)
  Poisson model: gamma(0.5, 0)
  Exponential model: gamma(0, 0)
Last two are not proper distributions
Enter in OpenBUGS as dgamma(0.5, 0.0001) and dgamma(0.0001, 0.0001)
Redo LOSP example problem from P-102 with Jeffreys priors

## Slide 28: Nonconjugate Priors – Lognormal Distribution
Generic databases often express uncertainty in terms of lognormal distribution
Experts often provide order-of-magnitude estimates, represented well by lognormal distribution
For these or other reasons, we may prefer a nonconjugate prior

## Slide 29: Lognormal Distribution
Definition of a lognormal distribution:
  X is lognormal(μ, σ2) if ln(X) is normal(μ, σ2)
Will encounter lognormal distribution in various areas of risk assessment
  Often used as a prior distribution in PRA, even though it is not conjugate
  Sometimes used as likelihood function (e.g., LOSP recovery time)
  Often used to model hazard (earthquake frequency) and fragility (probability of seismic failure) in seismic PRA

## Slide 30: Facts About the Lognormal Distribution
Median of X is eμ Mean of X is exp( + 2/2)
Variance of X is (mean)2[exp(2) – 1]
Error factor (EF) is defined as e1.645σ
Other ways to write EF (applies only to lognormal)
    EF = 95th/50th = 50th/5th = (95th/5th)1/2
Probability
where Ф is tabulated in HOPE, Appendix C
  Can also use =LOGNORMDIST(x, , ) in Excel
  or =NORMDIST(LN(x), , , TRUE)
Percentile
  Can use =LOGINV(p, , ) in Excel
Notes: Point out that mean is always > median

## Slide 31: Facts About the Lognormal Distribution
Lognormal distribution is determined (in general) by
  μ and σ2 (or  = 1/ σ2)
  Median and mean
  Median and variance
  Mean and variance
  Median and EF
  Mean and EF
SAPHIRE uses mean and EF

## Slide 32: Example Problem with Nonconjugate Prior
Interested in failure on demand for standby pump
Generic database represents uncertainty in p via lognormal distribution with
  mean of 0.003
  error factor of 10
Observe 0 failures in 36 demands
What is posterior mean of p?
What is the probability the posterior is p>0.01?
  Use the “step( )” function
Notes: Explain the step(e) function. Value of “1” when e>=0, 0 otherwise. Gives the probability of exceedance if used as step(p > 0.01).

## Slide 33: OpenBUGS Example with Nonconjugate Prior
Generic prior is lognormal w/ mean = 0.003 and EF = 10
Data is 0 failures in 36 demands
Section 3.2.3 in Textbook
binomial-lognormal-update.odc
Model {
mdp.fts ~ dbin(p.fts,n.fts) #Binomial distribution
p.fts ~ dlnorm(mu, tau) #Lognormal prior
sigma <- log(EF)/1.645 #Solve for using EF
tau <- pow(sigma, -2) #Lognormal parameter used by BUGS
mu <- log(prior.mean) - pow(sigma, 2)/2 #Solve for using lognormal parameters, prior mean
prob.exc <- step(p.fts – 0.01) #Calculate the probability p.fts > 0.01
}
data
list(mdp.fts=0, n.fts=36, prior.mean=3.E-3, EF=10)
Notes: Take time to point out the use of logical nodes in this script to translate mean and EF into mu and tau. Also discuss BUGS parameterization of lognormal distribution and list of script lines in text pages 33-34.

## Slide 34: DAG Model

## Slide 35: OpenBUGS Example with Nonconjugate Prior
Run this model with 100,000 samples (1,000-sample burn in)
  Posterior mean of p.fts = 0.0022
  Posterior 90% interval is (1.1E-4, 7.9E-3)

## Slide 36: BUGS Exercises with Nonconjugate Priors
A prior for  is taken as lognormal with a mean of 0.04/yr and an EF of 2.
  Find the 5th and 95th percentiles of this prior distribution.
  If 2 events are seen over a 7-yr period, update the prior distribution to find the posterior mean of .
  What is the probability of seeing 2 or more events in the next 7 years? (Instructor-led)
Notes: For first question, which is a first glance at model checking, point out how posterior mean is between prior mean (0.04) and MLE (0.29), but strongly influenced by prior distribution. Have students find 95th percentile of prior distribution (0.07). Draw DAG showing predicted event count, discuss use of step() function to find tail probability of posterior predictive distribution.

## Slide 37: BUGS Exercises with Nonconjugate Priors
A system has two redundant motor-driven pumps, each of which fails on demand with prior median probability 0.01 and upper bound probability 0.05, and a turbine-driven pump, which fails on demand with prior median probability 0.03, and upper bound probability 0.08. The motor-driven pumps each can supply 50% of the system needs, and the turbine-driven pump can supply 100% of the system needs. Assume that each pump fails independently of the others. Assume that the epistemic uncertainty in each pump’s failure probability is lognormally distributed.
  Write the expression for failure of the system, in symbols. Caution: think about state-of-knowledge correlation.
  What is the mean probability that the system fails on demand if there has been 1 turbine-driven pump failure in 28 demands and 0 motor-driven pump failures in 64 demands?
  What is the 95th percentile (upper bound) of this probability?
  NOTE: Error Factor formulas and scripts are on page 33-34 of the textbook

## Slide 38: Miscellaneous BUGS Exercises
Pipes are designed to contain pressurized fluid. Let PF denote the pressure at which a pipe fails. This failure pressure is treated as random, corresponding to variability in the strength of pipes. Assume that PF is lognormally distributed, with median = 975 psig and  = 0.4. If a pipe experiences a pressure of 1200 psig, what is the probability that the pipe fails? Repeat the above problem, but now model the system pressure (to which the pipe is exposed) as being normally distributed with a mean of 1200 psig and a standard deviation of 100 psig.
  Note: If median and sigma are given, the lognormal parameters script is:
  mu <- log(median)
  tau <- pow(sigma,-2)

## Slide 39: Miscellaneous BUGS Exercises
A diesel generator is required to have a failure probability (on demand) of 0.05 or less. The facility PRA has estimated the failure probability as being beta-distributed with a mean value of 0.027 and  = 54. If we observe 3 failures in 27 tests of the EDG, what is the probability that this criterion is met?
A licensee is updating the initiating event frequency for loss of turbine-building cooling water. Their prior distribution is lognormal with a mean of 0.02/yr and an error factor of 10. They have observed no losses in 27.5 Rx-yrs. Carry out the update and find the posterior mean and 90% interval.

## Slide 40: Miscellaneous BUGS Exercises
In 60 demands of an AFW turbine-train, there were two failures to start. The unknown parameter of interest is p = Pr(failure to start). Assume a beta prior distribution for p, with  = 0.6 and  = 10.2. What is the posterior mean? Find the 5th and 95th percentiles of the posterior distribution.
In 20 reactor-calendar years (17.3 reactor-critical years), there were 2 initiating events involving total loss of feedwater flow. The unknown parameter of interest is , the frequency of events per reactor-critical year. Assume a gamma prior distribution for , with  = 0.8 and  = 10.6. Find the posterior mean and 90% credible interval for .

## Slide 41: Common-Cause Failure
Observe N failures in component group of size k
  n1 involve one component, n2 involve 2, etc.
  In alpha-factor model, failure counts have multinomial distribution with (vector) parameter α

## Slide 42: Common-Cause Failure
Conjugate prior for α is Dirichlet(θ)
In equation form:

## Slide 43: DAG Model

## Slide 44: CCF Example
Group of size 3, n1 = 200, n2 = 5, n3 = 1
Usual noninformative prior is Dirichlet(1, 1, 1)
  Multivariate analog of uniform distribution
  Mean of each alpha-factor is 0.5
  Jeffreys prior is Dirichlet(0.5, 0.5, 0.5)
Find posterior mean and 90% interval for alpha-factors
Section 10.5 in Textbook

## Slide 45: CCF Example
BUGS script
Multinomial CCF Example.odc
Model {
n[1:groupsize] ~ dmulti(alpha[1:groupsize], N)
N <- sum(n[1:groupsize])
alpha[1:groupsize] ~ ddirich(theta[])
sum <- alpha[1] + alpha[2] + alpha[3]
}
data
list(n=c(200, 5, 1), groupsize=3, theta=c(1,1,1))

## Slide 46: CCF Example
Results