## Slide 1: Section 10: Misc. Bayesian Examples
Will illustrate
  Checking to see if a failure rate of a component has changed
  Determining the probability of meeting a reliability goal
  Modeling “extreme” event frequencies
  Using OpenBUGS for solving Markov Models
  Batch script running OpenBUGS
  R and RStudio for statistical analysis
  JAGS and STAN

## Slide 2: Check to see if a Failure Rate has Changed

## Slide 3: Checking the Assumption of a Higher Failure Rate
A new component is used at a plant, but we have seen a couple of failures of this component
One check we may want to do is question the validity of the assumption that the new component does have a higher failure rate than the old component
We need to know
  What the old rate was
  What is our estimate of the new rate
We can then calculate Pr(λhigh > λold)

## Slide 4: Checking the Assumption of a Higher Failure Rate
Assume the old component has a Gamma(1.5, 300,000 hrs) distribution for λold
To determine the distribution of λhigh, we will perform a Bayesian update
  Assume a Poisson model, a Jeffreys prior, and two failures in 41,861 hours of operation
The script (next page) can be used to find:
Pr(λhigh > λold) = 0.99
  There is a significant evidence to suggest that the new failure rate is probabilistically higher than the old failure rate.

## Slide 5: OpenBUGS Script
model {
# Poisson dist. for number of events seen
x.new ~ dpois(mean.new)
# Poisson parameter for OpenBUGS
mean.new <- lambda.new*time.new
# Jeffrey's prior for Poisson
lambda.new ~dgamma(0.5, 0.0001)
# The old distribution
lambda.old ~ dgamma(alpha, beta)
# STEP function to calculate Pr(lambda.new >= lambda.old)
test <- step(lambda.new - lambda.old)
}
data
list(x.new=2, time.new=41861, alpha=1.5, beta=300000)
Failure Rate Assumption Check.odc

## Slide 6: Probability of Meeting a Reliability Goal

## Slide 7: Determining the probability of meeting a reliability goal
We are going to replace our emergency diesel generators with fuel cells, but we wish to have the new system meet a reliability goal before the switch
Our reliability goal is the new system should have a reliability of 0.99 with a probability of 95%
  In other words, the failure
  probability should be less
  than 0.01 with
  probability 0.95

## Slide 8: Determining the probability of meeting a reliability goal
We test the fuel cell system and find one failure in 250 system demands
Calculate
  The probability we meet the goal
  The probability that we will see one or more failures in the next 250 demands on the system

## Slide 9: Reliability Goal OpenBUGS Script
  The probability we meet the goal = 83%
  The probability that we will see one or more failures
  in the next 250 demands on the system = 64%
model {
x ~ dbin(p, N) # Number of failures in N demands
p ~ dbeta(0.5, 0.5) # Jeffrey's prior
x.rep ~ dbin(p, N) # Replicated data
# step(x.rep - z) gives Pr(x.rep >= z)
# step(z - x.rep) gives Pr(x.rep <= z)
p.0 <- step(0 - x.rep) # Prob 0 failures (in N demands)
p.not0 <- 1 - p.0
p.1 <- step(x.rep - 1) # Prob 1 or more failures (in N demands)
p.not1 <- 1 - p.1
p.notgoal <- step(p - goal) # Prob not meeting goal
p.goal <- 1 - p.notgoal # Prob meeting goal
p.goal.check <- step(goal - p) # Prob meeting goal
}
data
list(N=250, x=1, goal=0.01)
Probability of Meeting Rel Goal.odc
Notes: 391 samples with only 1 failure required to meet goal and confidence.

## Slide 10: Reliability Goal Results
node mean 5th median 95th
p 0.0059 7.1E-4 0.0047 0.0154
p.0 0.356
p.1 0.644
p.not0 0.644
p.not1 0.830
p.goal 0.830
p.goal.check 0.830
p.notgoal 0.170
x.rep 1.49 0.0 1.0 5.0

## Slide 11: Modeling “Extreme” Events

## Slide 12: Modeling the initiator or enabler
Extreme events such as historic floods may be enabled by events such as “smaller” storms that cause ground saturation preceding larger precipitation events
We need to understand the frequency of these events
  It is not enough to focus on “100 year” events
  Bayesian inference can help here
Let us describe an example of how to model these types of extreme events
Approach described in Chapter 13

## Slide 13: A Synthetic Extreme Events Example
First, we’ll present an example where the underlying model is known:
      M = magnitude of event in meters
      IR = return interval measured in years
  Want to predict events that have not been “seen”
From this model we can determine the exact magnitude M of an event for any return interval and compare to the Bayesian GEV predictions.

## Slide 14: Data for the initiator
Sample extreme events data:

## Slide 15: Bayesian modeling for the initiator
From this data we wish to estimate the magnitude at 2,000 and 10,000 year events
Create an OpenBUGS script (next page) to perform the Bayesian inference
  Uses a Generalize Extreme Value (GEV) model

## Slide 16: OpenBUGS script for the initiator
The GEV Model
The Priors
The Data
P(x) = 1 - exp[-T * λ] = 1 - exp[-(1 yr) * 1/IR]
GEV Example 1.odc
Notes: P(x) = 1 - exp[-T * λ] = 1 - exp[-(1 yr) * 1/IR], return interval MTTE = 1/λ

## Slide 17: Synthetic data example results
Running the script indicates the average magnitude of a 2,000 year event is 2.14 m while for a 10,000 year event is 2.52 m.
OpenBUGS results show the predicted event magnitude (average, box points and associated 90% intervals (shaded area)

## Slide 18: Probable Maximum Precipitation event example
Inference related to severe rainfall events around a specific location (e.g., a plant site near a major river)
A Probable maximum precipitation (PMP) for a sample facility is defined as
  3 day storm that drops 6.44 inches, then a 3 day break, followed by a 3 day storm that drops 16.34 inches of rain
For our rainfall event, we assume the two storm events are not independent (a hurricane or large storm)
  We will assess the frequency of 6.44” + 16.34” or 22.8” of rain falling in the 9 day window

## Slide 19: Data for the initiator
Information on rain storms is available from organizations such as the National Oceanic and Atmospheric Administration (NOAA)
  For example, information for a particular area of the U.S from the publically-available Precipitation Frequency Data Server
  Bold lines are provided. We interpolate for the 9 day data.
Our focus

## Slide 20: Bayesian modeling for the initiator
We need to estimate recurrence interval for a 22.8” rain fall event within a 9-day window
Create an OpenBUGS script (next page) to perform the Bayesian inference
  Uses a Generalize Extreme Value (GEV) model

## Slide 21: OpenBUGS script for the initiator
GEV Model
The Priors
The Data
GEV Example 2.odc

## Slide 22: The results for the initiator
The results show the recurrence frequency for 22.8 inch rain events (in a 9-day window) is approximately 1,000,000 years

## Slide 23: The results for the initiator
The uncertainty at this return period

## Slide 24: Using the results for the initiator
The resulting information could be integrated directly into a PRA
The rainfall event (that is produced stochastically) would impact the plant buildings and SSC
  Still need to determine what, if anything, happens as a result of the initiator

## Slide 25: Using OpenBUGS for Markov Models

## Slide 26: Markov Model
In general, a Markov Model consists of three things
  A set of states (e.g., component A is failed, component A is working)
  Transitions between states (e.g., how do we get from one state to another state)
  The rate of transition between the states
Examples of the state for any one component
  Failed
  Operating
  In repair
  In maintenance
  In standby

## Slide 27: Graphical Depiction of Markov Model
Standard notation is to have
  States as circles
  Transitions as arc

## Slide 28: Simplest Model is for Single Component
Failure rate is λ
P0(t) is the probability of being in State 0 at time t
P1(t) is the probability of being in State 1 at time t
Also need to define the initial conditions
  Assume the component is working at t=0, so
    P0(0) = 1
    P1(0) = 0
  But after t = 0, the transition probability during the next small time increment (dt) is = λdt

## Slide 29: The Math for the Single Component
For each time increment (dt) we “lose” λdt worth of probability from State 0
  Consequently, we can describe the change in the State 0 probability
  Change in State 0 Probability =
  - (Probability in State 0) x (Probability moving to State 1 | in State 0)
  Or
  dP0 = - (P0) λdt
  Note the minus sign indicates we are “losing” probability (in State 0) since we can only move in one direction in this Markov Model
  The DE for this state is then dP0 /dt = - (P0) λ

## Slide 30: The Math for the Simple Component
The single component with no repair gave us a simple set of DEs
  dP1 /dt = - (P1) λ
  dP2 /dt = (P1) λ
When we solve these DEs, we find
  P1(t) = e-λt
  P2(t) = 1 – P1(t) = 1 - e-λt
It is important to be able to write down the system of DEs
  However, rather than solving them using methods such as Laplace Transforms, we will use OpenBUGS

## Slide 31: How Can We Use OpenBUGS to Solve This?
OpenBUGS includes a built in ordinary different equation (ODE) solver using a single function call
solution[1:n, 1:dim] <-
ode(init[1:dim], time[1:n], D(P[1:dim],t), t0, tolerance)
Initial Conditions
Time Points
The Equations
Initial Time
Tolerance
So what are all of these terms inside the “ode” function?

## Slide 32: OpenBUGS ode() Inputs (When Solving Markov Models)
Initial Conditions
  A vector (of size dim) corresponding to the initial state probabilities at t=0 (generally we start in state 0 with probability 1.0)
Time Points
  A vector (of size n) with the time points at which the ODE will be evaluated
The Equations
  A vector (of size dim) containing the ODE equations
Initial Time
  The starting time at which the ODE will be evaluated (usually 0)
Tolerance
  A small value (say 1E-3 or 1E-4)

## Slide 33: Solve the Simple Component (no repair)
Lambda in this example with have a distribution
  Lognormal(μ=-8, σ=0.5)
    Lognormal(-8, 4) in OpenBUGS
  What is the mean of this distribution??
What is the Pr(failure|8000 hrs)?
Answer  Run OpenBUGS
  File: Solve Markov Model – Single Component No Repair
  Note: These calculations can be SLOW
λ

## Slide 34: Step-by-Step for the Simple Component (no repair)
Dissect the OpenBUGS script
First we create a set of “evaluation points” which are really a set of times (in this example)
grid[1]=10, grid[2]=20, grid[3]=30, etc.
  # Create a set of grid values in which to evaluate the ODE
  for (i in 1:n) {
  grid[i] <- 10*i
  }

## Slide 35: Step-by-Step for the Simple Component (no repair)
Second we define the ODEs
  D(P[1], t) = dP1 /dt = - λ P1
  D(P[2], t) = dP2 /dt = λ P1
Third, define the distribution for λ
# The ODE
solution[1:n, 1:dim] <- ode(init[1:dim], grid[1:n], D(P[1:dim], t),
t0, tolerance)
D(P[1], t) <- (-lambda) * P[1]
D(P[2], t) <- lambda * P[1]
# Rather than a single value, assume lambda has a distribution
lambda ~ dlnorm(-8, 4)

## Slide 36: Step-by-Step for the Simple Component (no repair)
Fourth, define the initial probabilistic conditions
Lastly, define the nodes that contain “the results”
# Set the initial values such that P1(0) = 1 and P2(0) = 0
init[1] <- 1; init[2] <- 0
# Failure Probability is found by State 2
# (at time=8000, which is point 800)
State.2 <- solution[800, 2]
# Solve using the "solution" for exponential CDF
# F(t)=1-exp(-lambda*t)
Pr.failure <- 1 - exp(-lambda*MT)
Solve Markov Model – Single Component No Repair.odc

## Slide 37: Results for the Simple Component (no repair)
Running 10,000 samples
These results are the probability of failure F(t) or the Unreliability
RESULTS
mean sd 2.5pc 50pc 97.5pc
Pr.failure 0.8991 0.1012 0.6347 0.932 0.9993
State.2 0.8991 0.1012 0.6347 0.932 0.9993

## Slide 38: Results for the Simple Component (no repair)
The pdf (density) for State 2 at 8000 hours

## Slide 39: Batch Script Running of OpenBUGS

## Slide 40: Batch Script Mode
Now that you’ve been clicking on dialog boxes all week long… here’s a way to run OpenBUGS in a reproducible, automated way
Script running of OpenBUGS allows:
  Automation of routine analyses
  Running OpenBUGS from other programs
Can run from the OpenBUGS interface
Can use Windows or Linux
Typically runs a lot faster than using OpenBUGS manually

## Slide 41: Batch Script Setup
For simple path assignment, place the expanded OpenBUGS folder in the same root directory as the BUGS files you want to run.
  Doing this will allow you to use the “../” text seen on the following slides in your path to make the path assignment easier
Data must be in a separate file and not in columnar format
Inits must also be in a separate file
A list of scripting commands is in the Help file / Manual

## Slide 42: Batch Scripting Basic Commands
The following commands are a good start for script running
Comment out what you don’t need (e.g. modelInits() for a model you aren’t providing user initial values for
ModelScript # Keyword
modelDisplay('log') # Display in the log
modelPrecision (4) # Set significant digits
modelCheck('../BUGS files/EDG FTS.odc') # Check the model
modelData('../BatchBUGS/EDG FTS data.txt') # Load the data
modelCompile (1) # Compile this many strings
modelInits('../BatchBUGS/EDG FTS inits.txt‘,1) # Load inits for string 1
modelInits('../BatchBUGS/EDG FTS inits.txt‘,2) # Load inits for string 2

## Slide 43: Batch Scripting Basic Commands
modelUpdate(1000, FALSE) # Burn in updates before monitoring node
samplesSet(p) # Set node to monitor
modelUpdate(100000, 1, 10000, FALSE) # Run 100k iterations, thinning set to 1, refresh set to 10000, over-relax set to False, last 3 optional
samplesStats('*') # Print samples statistics
samplesDensity(p.value) # Print the pdf for this node
#modelExternalize('restart') # Used to restart when called from other programs
#modelSaveLog('BUGSModelLog.txt') # Save text output log, no images
#modelSaveLog('BUGSModelLog') # Save .odc output log, with images
modelQuit(N) # Y=erase log, N=leave log open in OpenBUGS, blank will present a dialog box

## Slide 44: Batch Script Example
A folder called BatchBUGS is placed at the same level as OpenBUGS expanded folder for this to work
Click on Info menu then Clear Log
Drag and drop “Script - batch for mixture priors.txt” onto the OpenBUGS screen

## Slide 45: The Mixture Priors Script
Review the scripting commands on the next slides for the Mixture Priors models run in the course slides Section 8
Refer to the basic scripting commands given in the previous slides or the Help manual in OpenBUGS for the functions
Note that the script runs sequentially and the second modelCheck command looks for the “model” keyword in the new model script
  This means we can get both sets of output for the mixture priors on one log

## Slide 46: The Mixture Priors Script
ModelScript
modelDisplay('log')
modelPrecision (4)
modelCheck('../BUGS files/mixture priors - prior.odc')
modelData('../BatchBUGS/mixture priors - prior data.txt')
modelCompile (1)
modelGenInits()
modelUpdate(1000, FALSE)
samplesSet(p.avg)
samplesSet(p)
samplesSet(r)
modelUpdate(100000, 1, 10000, FALSE)

## Slide 47: The Mixture Priors Script continued
samplesStats(p.avg)
samplesDensity(p.avg)
samplesDensity(p)
samplesDensity(r)
modelCheck('../BUGS files/mixture priors.odc')
modelData('../BatchBUGS/mixture priors data.txt')
modelCompile (1)
modelGenInits()
modelUpdate(1000, FALSE)
samplesSet(p.avg)
samplesSet(p)
samplesSet(r)

## Slide 48: The Mixture Priors Script continued
modelUpdate(100000, 1, 10000, FALSE)
samplesStats(p.avg)
samplesDensity(p.avg)
samplesDensity(p)
samplesDensity(r)
#modelExternalize('restart')
#modelSaveLog('BUGSModelLog.txt')
#modelSaveLog('BUGSModelLog')
modelQuit(N)

## Slide 49: Run the Mixture Priors Script
Click on Model menu then Script
  The open script in the OpenBUGS interface screen will run

## Slide 50: Mixture Priors Script Log - Prior

## Slide 51: Mixture Priors Script Log -Posterior

## Slide 52: R and RStudio for Statistical Analysis

## Slide 53: R Programming Language
R is an open-source programming language
Based on S programming language created by John Chambers of Bell Labs ~1988
R Project developed in 1990s, first stable beta in 2000 by Ross Ihaka and Robert Gentleman of University of Auckland, NZ
Strengths
  Number of packages (11,900+)
  Statistical and graphical techniques
  Bayesian, statistical tests, clustering, linear and nonlinear modeling
  Calls for C, C++, and Fortran code linkage
  C, C++, NET, Java, and Python can manipulate R objects directly
Weaknesses
  Not built for speed
  Default interface
  The future may be Julia

## Slide 54: RStudio
Currently most popular open source integrated development environment for R
  Makes R easier, more reproducible more documentable as analysis tool
  Other GUIs are available such as Tinn-R
Features
  R console (pretty much the only thing you get in R itself)
  Syntax highlighting editor
    Documents your R language session (script) for easy duplication
    Write or view code in other languages like BUGS to use in R
  File management, plotting, history, and debugging

## Slide 55: Downloading R
Search R project
Follow download R link and choose a mirror site
  Oregon State University appears closest

## Slide 56: Downloading R
Download the pre-compiled binaries in the top box for your platform
Choose “base” or “install R for the first time”

## Slide 57: Downloading R
Choose “base” or “install R for the first time”
Defaults OK in install
  32bit, 64bit
  Etc…
Requires admin

## Slide 58: Setting up R
R looks for packages to run in folders on your computer that end in \\R\win-library
Create this folder in your Documents folder (the install may have already done so)
  \\Users\<you>\Documents\R\win-library\<version>
  \\Users\<you>\Documents\R\win-library\3.4
Documents folder will be the default working directory
R has default packages in its install library
R will look in the win-library for other packages to load

## Slide 59: Downloading RStudio
Download the open source edition

## Slide 60: Downloading RStudio
The zip can be expanded and used without admin privileges

## Slide 61: RStudio
White default background
Tools >> Global Options to change

## Slide 62
RStudio panels

## Slide 63
R session starts with setting up a working directory
This tells R where to find all of the files used in the session

## Slide 64: Steps to Starting an R Session
Set working directory
  Commands to know
    getwd()
    setwd()
Load packages
  library(package name)

## Slide 65: Downloading a Package (Windows machines)
Download to My Documents/R/win-library folder
  R will look for packages in a folder with R/win-library
Comprehensive R Archive Network (CRAN)
  11,900 plus packages
  Can download binaries through R (requires admin rights) or outside of R

## Slide 66
CRAN Search

## Slide 67
CRAN Package Page

## Slide 68: Package Binary Placement
Some packages extract with sub-folder versions and R may not recognize them, such as the CODA package
Just move coda to the 3.4 folder
  Same level as rjags
  Coda_0.19-1 only contains coda

## Slide 69: Console Entry Starting an R Session
Entry can be cut and paste from editing pane to console
  Provides repeat-ability and quick return to analyses
  Can save as .r extension (R script)
Terminal tab is for access to the system shell for “advanced users”

## Slide 70: RStudio Packages Tab
Packages tab can load and detach packages by just clicking on the box.
Update package will do so in R environment and you’ll need admin privileges
  It checks for updates available

## Slide 71: R Language Syntax
There’s a ton of help online
Variables generally use leftward “<-” or rightward “->” operator. Equal sign works sometimes
  Operator points to the variable
  X <- 7
  42 -> Y
List or vector uses c()
  list_a <- c(1, 3, 5, 7)
  list.b <- c(“use”, “R”)
Variables limited to dots, underscores and alphanumeric
Syntax for package commands are both in the console popup help and in the package documentation

## Slide 72: RStudio and R in Operation
R script in upper left window
Console in lower left window
  Cut and paste R script here
Global Environment in upper right window
Plots in lower right window

## Slide 73: RStudio Using a Package
Using script in upper left

## Slide 74: RStudio Using a Package
Set the working directory
  Used thumbdrive here
  Note forward slashes
Attach rjags package
Program will auto-suggest and show syntax

## Slide 75: RStudio Using a Package
Text editor

## Slide 76: RStudio Using a Package
Using script in upper left
Can highlight and CTRL+Enter
Script runs in lower left and shows results
Note objects in Environment can be viewed
History in upper right shows history of commands without results

## Slide 77: RStudio Example
Script acts as a running log of analyses

## Slide 78: Bayesian Inference Programs in R
OpenBUGS
JAGS
STAN

## Slide 79: OpenBUGS
A selection of packages available
  R2OpenBUGS
  BRugs
Syntax is the same as for the stand alone interface
New commands specific to the packages are well defined in the package documentation
Similar syntax to Batch Bugs demonstrated in the class

## Slide 80: JAGS
Just Another Gibbs Sampler
Developed and maintained by Martyn Plummer
More current support than OpenBUGS
Runs in the R environment through interface packages
  RJAGS
  R2JAGS
Nearly identical syntax to OpenBUGS, however there are differences
Vast help through Source Forge Q&A files

## Slide 81: Stan
Different sampling algorithms than OpenBUGS or JAGS
Uses Hamiltonian Monte Carlo to sample in sequences from a probability distribution
  Useful for models that have difficulty converging in OpenBUGS or JAGS
R package is RStan

## Slide 82: Summary
RStudio is a useful interface to use R
R requires admin rights
RStudio and R packages do not require admin rights
R script easily organizes and reproduces analyses
Very well supported with tons of help online
OpenBUGS runs in R environment, as does JAGS, a sister program to OpenBUGS which seems to run a little faster and has more current support
Stan is also a current highly supported Bayesian inference program that runs in R and useful for models that have problems converging