## Slide 1: Section 6: Uncertain Data
Problem: observed data are uncertain or “fuzzy”
  Interval-valued observations and other types of censoring
  Unclear whether failure occurred
  Number of demands not known with certainty
Will illustrate Bayesian approach to these problems
Section 10 in the Textbook

## Slide 2: When Durations are Uncertain
Consider following data for fire suppression time
Event | Duration (mins.)
1 | < 5
2 | < 5
3 | < 15
4 | 14
5 | 15
6 | 15
7 | 10 - 30
8 | 15
9 | 150
10 | 100 - 300
Notes: Point out how these data are uncertain.

## Slide 3: When Durations are Uncertain
Use simple model for T (fire duration)
  Tsupp ~ exp()
   is suppression rate, units of min-1
Data are interval-censored, meaning we only have an interval for some points
  Know duration was > lower bound time and < upper bound time
Handled in OpenBUGS by specifying
time.supp[i] ~ dexp(lambda)C(lower[i] , upper[i])
Specifying data
  If specific duration observed, set lower[i] = upper[i] = duration for that point
  No fixed time observed, set time.supp[i] = NA, lower[i] and upper[i] set to bounds of interval
    OpenBUGS imputes missing data using the likelihood function
Notes: Can also use the I() construct, as this was used by older versions of BUGS.
Imputes means OpenBUGS fills in the blanks with the predictive function.

## Slide 4: When Durations are Uncertain
OpenBUGS program
Case study for uncertain times.odc
model {
for (i in 1 : N) {
time.supp[i] ~ dexp(lambda)C(lower[i], upper[i]) #Exp. dist for times
}
lambda ~ dgamma(0.0001,0.0001) #Diffuse prior for Exp. parameter
}
data
list(time.supp=c(NA, NA, NA, 14, 15, 15, NA, 15, 150, NA),
lower=c(0 ,0 , 0 , 14, 15, 15, 10, 15, 150,100),
upper=c(5 , 5 , 15 , 14, 15, 15, 30, 15, 150, 300), N = 10)
inits (initial values)
list(lambda = 0.1)
list(lambda=0.01)
Notes: Script has data in columnar format for ease of presentation

## Slide 5: When Durations are Uncertain
Results

## Slide 6: When Durations are Uncertain
This is sometimes referred to as likelihood-based approach to uncertain data
  Observed time in interval [a, b] contributes e-λa – e-λb to the likelihood function in Bayes’ Theorem
Caution: cannot have too much censoring and still get sensible estimates
  If all durations are censored, cannot get meaningful estimate
Frequentist estimate is 0.0265/min, very close to posterior mean
  Expect values to be close with diffuse prior on 
  Frequentists cannot easily find uncertainty in estimate
Notes: Excel file uses Solver to find MLE.

## Slide 7: When Demands are Uncertain
Often a problem with components such as MOVs, where each demand may not be recorded
Handle in Bayesian approach by assigning a distribution to number of demands, n
  Uniform(a, b)
  Poisson()
Uniform(a, b)
  N is a discrete variable, so really want a discrete uniform distribution
  Can program this into OpenBUGS
  Easier to sample from continuous uniform distribution and round sample to nearest integer
    Endpoints are under-represented, but this is not usually a problem

## Slide 8: When Demands are Uncertain
Example: Assume prior distribution for MOV FTO is lognormal with mean = 0.003 and EF = 10
  Assume 1 failure is seen, and demands are not recorded, but are known to lie between 12 and 40
  OpenBUGS model
Uncertain demands – uniform.odc
model {
mov.fto ~ dbin(p,demands) #Binomial model for MOV FTO
p ~ dlnorm(-6.79, 0.5102) #prior for p (mean = 0.003, EF = 10)
demands.continuous ~ dunif(lower, upper) #Uncertainty in demands
demands <- round(demands.continuous) #Rounds to integer
}
data
list(lower=11.5001, upper=40.4999, mov.fto=1)
lower and upper set to include rounded numbers between 12 and 40.
Notes: Point out use of uniform distribution for demands in this program.

## Slide 9: When Demands are Uncertain
DAG model
Notes: Note that “demands” is now a stochastic node, where it was a constant node in earlier models.

## Slide 10: When Demands are Uncertain
Results
  Comparable to results with n set to mean value (26)
    Posterior mean somewhat sensitive to n, but uncertainty in p relatively insensitive to uncertainty in n
    In other words: failures have more of an effect on the posterior than demands do

## Slide 11: When Demands are Uncertain
Try same example, but with Poisson distribution for number of demands
  Use mean of 26 (same as previous example)
  Recall variance = mean for Poisson distribution  standard deviation = 5.1
Uncertain demands – Poisson.odc
model {
mov.fto ~ dbin(p,demands) #Binomial likelihood
p ~ dlnorm(-6.79, 0.5102) #prior for p (mean = 0.003, EF = 10)
demands ~ dpois(mu) #Poisson distribution for number of demands
}
data
list(mu = 26, mov.fto=1)

## Slide 12: When Demands are Uncertain
DAG model

## Slide 13: When Demands are Uncertain
Results
  Essentially the same as with uniform distribution for n

## Slide 14: When Failures Are Uncertain
Information from LERs and other information sources may not be clear enough to ascertain exact number of failures
Sloppy record-keeping may result in imprecise estimates
  Analogous to rounding of value
Two approaches
  Posterior-averaging
  Likelihood-based

## Slide 15: Posterior-Averaging Approach
Analyst must develop subjective prior distribution for number of observed events
Example 1: plugging of service water strainers
  Inspection Report (IR) describes 7 plugging events over time period of interest
  3 of these may not have been complete plugging events from perspective of PRA model
  Therefore, actual number of events is 4, 5, 6, or 7
  Total operation hours of all strainers in the study was 48180 hr.

## Slide 16: Posterior-Averaging Approach
Analyst, by poring over the IR, and applying expert knowledge, has come up with following distribution for actual number of complete plugging events:
Pr(x = 4) = 0.75
Pr(x = 5) = 0.15
Pr(x = 6) = 0.075
Pr(x = 7) = 0.025
Note that probabilities must sum to unity!

## Slide 17: Posterior-Averaging Approach
OpenBUGS program for Example 1
uncertainty in Poisson event count.odc
model {
#Use following if data are observed with subjective probability specified by p[] vector
for(i in 1:N) {
x[i] ~ dpois(mu[i])
mu[i] <- lambda[i]*time.exp
lambda[i] ~ dgamma(0.5, 0.0001) #Jeffrey’s prior for lambda
}
lambda.avg <- lambda[r] #Overall composite lambda, monitor this node
r ~ dcat(p[])
}
Data
list(x=c(4,5,6,7), p=c(0.75, 0.15, 0.075, 0.025), N=4)
list(time.exp=48180)

## Slide 18: Posterior-Averaging Approach
Results for Example 1

## Slide 19: Posterior-Averaging Approach
Example 2: MOV failures in 381 demands
  Because of vagueness of problem reports, can’t tell if actual number of failures was 3, 4, 5, or 6
  Analyst develops following distribution:
  Pr(x = 3) = 0.1
  Pr(x = 4) = 0.7
  Pr(x = 5) = 0.15
  Pr(x = 6) = 0.05

## Slide 20: Posterior-Averaging Approach
OpenBUGS program for Example 2
uncertainty in binomial failures.odc
model {
for (i in 1:N) {
x[i] ~ dbin(p[i], D)
p[i] ~ dbeta(0.5, 0.5) #Jeffrey’s prior for beta distribution
}
p.avg <- p[r] #Composite posterior, monitor this node
r ~ dcat(q[])
}
Data
list(x=c(3,4,5,6), q=c(0.1, 0.70, 0.15, 0.05), N=4)
list(D=381)

## Slide 21: Posterior-Averaging Approach
Results for Example 2

## Slide 22: Likelihood-Based Approach
Revisit same examples, but treat number of failures as “missing”, but known to be in the interval [4, 7] for Example 1 and [3, 6] for Example 2.
OpenBUGS program for Example 1
uncertainty in Poisson event count.odc
Number of Poisson events is uncertain
model {
x ~ dpois(mu)C(lower, upper) #Use for likelihood-based approach
mu <- lambda*time.exp
lambda ~ dgamma(0.5, 0.0001) #Jeffreys prior for lambda
}
Data
list(x=NA, lower=4, upper=7)
list(time.exp=48180)
Notes: Note that this approach treats data as interval-censored. This is different than the “likelihood-averaging” approach proposed by Frank Groen and Ali Mosleh. This latter approach is not covered in this course.

## Slide 23
Results for Example 1
Likelihood-Based Approach

## Slide 24: Likelihood-Based Approach
OpenBUGS program for Example 2
Number of binomial failures is uncertain
model {
x ~ dbin(p, D)C(lower, upper) # Likelihood-based approach
p ~ dbeta(0.5, 0.5) # Jeffrey's prior
}
data
list(x=NA, lower=3, upper=6)
list(D=381)
uncertainty in binomial failures.odc

## Slide 25: Likelihood-Based Approach
Results for Example 2